## Slide 1: htb — Connectivity Imaging Toolbox
Digital Twining for optogenetic protocol design

## Slide 2: Protocol choice determines success — not hardware
The Problem
Three coupled problems:
Spatial encoding — which cells to stimulate together so individual contributions can be separated
Temporal encoding — what waveform shape and duration to use given indicator kinetics
Robustness — does the protocol work across different preparations, not just one network?
Poor protocol choice → F1 below 0.3 on perfectly good hardware.
htb solves this by simulating the full measurement chain and searching protocol space with Bayesian optimisation.
Each trial evaluated on 5 independent networks — mean F1 is quality, std F1 is robustness.
htb bootstraps protocol tuning
for better experimental results

## Slide 3: System Overview
Architecture
Six-layer stack — runners delegate down, results surface up
Runner Scripts
run_sweep · run_balanced_sweep · run_pipeline · run_joint · run_drug_screen · run_variability · run_sensitivity
Analysis Layer
ProtocolOptimizer · BalancedOptimizer · PrepVariability · SensitivityAnalyzer · ConnectivityPipeline · SinglePassOptimizer
Simulation Layer
Simulator — builds E/I network, runs Numba JIT physics, applies neuropil contamination, delegates mask logic
Mask Layer
HadamardMask · SingleCellMask · RandomSubsetMask · MultiScaleHadamardMask · SimplexMask
Protocol &amp; Parameter Layer
BioParams · StimProtocol · HadamardDesign · AnalysisConfig
Numba JIT acceleration: ~50–100× speedup vs NumPy. ~10s warmup on first run, cached thereafter.

## Slide 4: Biophysical Simulation Model
Simulation
What the simulator models
E/I network
Random cell positions, synaptic weights, conduction delays
Indicator dynamics
Biexponential rise/decay from BioParams
Neuropil contamination
F_obs[i] = F_soma[i] + r × Gaussian-avg(neighbors) r ≈ 0.7 for 2-photon
Shot + read noise
noise_sigma — calibrate from dark frames
Opsin drive
r_stim = power × opsin_sensitivity — calibrate from patch-clamp power series
Simulation pipeline
1. Build random E/I network
Cell positions, W matrix, synaptic delays
2. Mask: unit assignment + stim_profile
Which cells are illuminated in each pattern
3. Build light drive r_light (JIT)
N_cells × N_t array, waveform-shaped per trial
4. Neural simulation (JIT)
Spikes → Ca → fluorescence → dF/F
5. Extract responses + reconstruct C
Mask matched filter or least-squares
6. Score vs W_unit_weights
weight_corr + E_f1 + I_f1

## Slide 5: Spatial Encoding Strategies
Masks
Hadamard (recommended for E/I)
Cells → spatial blocks. Binary S-matrix patterns. Matched filter reconstruction. N patterns for N blocks. Use finest block size from recommended_block_sizes() for best E/I separation.
Single Cell
One pattern per cell — cleanest E/I separation, direct readout. Cost: N_cells patterns per rep. Best for validation and small networks (N ≤ 80).
Mask selection rule:
Balanced sweep → fine-scale HadamardMask
Validation → SingleCellMask
Random Subset
~50% of cells ON per pattern. Least-squares reconstruction. Separates E/I without spatial structure. Requires n_patterns ≥ 4 × N_cells and short ISI.
Simplex (real data)
Blob-based patterns from widefield pre-movie. Simplex vertex design minimises pairwise overlap. Run run_premovie.py first to detect cell positions, then load blobs.npz.

## Slide 6: Balanced E/I Recovery
Balanced E/I
The asymmetry problem
Inhibitory cells are ~20% of neurons — their signal is diluted when grouped into spatial blocks.
A threshold tuned to detect the majority E class systematically misses smaller I signals.
Standard composite score weights I_f1 at only 15%, reinforcing the asymmetry.
The solution: balanced_ei_f1
Independent threshold sweeps per class — E and I each find their own best threshold from quantiles of |C|.
Macro averaging:
balanced_F1 = 0.5 × E_F1 + 0.5 × I_F1
Equal weight regardless of class size.
Fine-scale HadamardMask minimises E/I mixing within blocks — use recommended_block_sizes()[-1].
Objective
final_score =
balanced_F1 × (1 − w × t_norm)
t_norm = experiment_time / budget
duration_weight:
0.0 → maximise F1 regardless of time
0.3 → mild efficiency pressure (default)
1.0 → maximise F1 per unit time
Output: Pareto frontier of time vs balanced F1, E vs I scatter, robustness panel.

## Slide 7: Pipeline Workflows
Workflows
run_sweep
+ run_variability
Connectivity only
1. Bayesian protocol search (Optuna TPE, 8 parameters)
2. Validate F1 across 50+ simulated preps
3. Sensitivity analysis — rank which BioParams matter
Typical time: 5–15 min
Output: best StimProtocol
run_balanced_sweep
Balanced E & I recovery
1. Fine-scale HadamardMask
2. Cross-network eval on 5 networks per trial
3. Duration-efficiency tradeoff (duration_weight)
4. Pareto frontier output
Typical time: 30–60 min
Output: Pareto plot + best protocol
run_pipeline
/ run_joint
Connectivity + PSP shapes
Stage 1: Hadamard sweep → connectivity matrix C
Stage 2: prior-informed targeted PSP — stimulate only known sources per target (5–10× fewer trials)
Typical time: 10–60 min

## Slide 8: Cross-Network Evaluation
Validation
Why cross-network, not cross-validation?
5-fold CV on a single simulation splits trials from one fixed network.
It tests data efficiency — how many reps you need — but not generalisation.
Every fold trains and evaluates on the same cells with the same weights.
Cross-network evaluation runs each candidate protocol on 5 independently sampled networks: different cell positions, different synaptic weights, different random seeds.
This directly answers: will this protocol work on a new animal or slice?
Mean F1 across networks = protocol quality
Std F1 across networks = prep-to-prep robustness
A protocol scoring 0.80 ± 0.03 is far more deployable than one scoring 0.85 ± 0.18.
Design properties
Fixed eval seeds:
Seeds 100–107 are fixed across all Optuna trials so every candidate protocol is scored on exactly the same networks. Prevents lucky network draws inflating scores.
Separate from TPE seeds:
rng_seeds [7, 42, 123...] drive the Optuna sampler, not the evaluation. The sampler never sees the networks it is scored on.
n_eval_seeds:
3 — fast, catches failures
5 — recommended default
8 — final validation runs

## Slide 9: Cross-Network Evaluation
Validation
Candidate protocol is evaluated on 5 independently sampled networks
StimProtocol
candidate
Network seed=100 (new cells, new W)
F1 = X.XX
Network seed=101 (new cells, new W)
F1 = X.XX
Network seed=102 (new cells, new W)
F1 = X.XX
Network seed=103 (new cells, new W)
F1 = X.XX
Network seed=104 (new cells, new W)
F1 = X.XX
Score = mean F1
Robustness = std F1
Low std = protocol generalises to new animals. Eval seeds (100–107) are fixed across all Optuna trials — every protocol is scored on the same set of networks.

## Slide 10: Scoring Metrics & Roadmap
Metrics, Roadmap
Standard composite score
score = 0.50 × weight_corr + 0.35 × E_f1 + 0.15 × I_f1
Used by run_sweep, run_pipeline, run_joint.
Balanced E/I F1
balanced_f1 = 0.5 × E_f1 + 0.5 × I_f1
Independent threshold sweeps per class. Used by run_balanced_sweep.
Score interpretation:
> 0.8 — Excellent: reliable for drug screens and comparisons
0.6–0.8 — Good: suitable for most connectivity analyses
0.4–0.6 — Marginal: increase reps or recalibrate BioParams
&lt; 0.4 — Poor: check opsin sensitivity, noise, or protocol bounds
Note: F1 values reported are oracle estimates (best threshold over ground truth). They are upper bounds on deployment performance.
Next 1–3 months:
Biological variability model
Sample BioParams from a prior distribution per eval seed so cross-network eval also covers parametric uncertainty.
PSP protocol optimiser
Dedicated run_psp_sweep.py — search stim_dur, ISI, power for Stage 2 given a fixed Stage 1 result.
LASSO reconstruction
AnalysisConfig.use_lasso already stubbed. Sparse reconstruction improves I recovery in low-SNR conditions.

## Slide 11: Protocol Design for Maximal E/I Network Recovery – One protocol to rule them all
Results
BALANCED SWEEP — RESULT
Final score: 0.2746 (duration_weight=0.30)
Balanced F1: 0.392 ± 0.033 (5 networks)
E F1: 0.684 (~301 true E connections)
I F1: 0.295 (~67 true I connections)
Experiment time: 859s (100% of 100s budget)
N patterns: 127 × 3 reps
Protocol: ramp_down n=5 duty=0.34 amp=0.64→0.02 pre=0.27s dur=1.80s isi=2.25s pwr=1.74mW/mm²
════════════════════════════════════════════════════════════════════
Best protocol (paste into run_drug_screen.py / run_variability.py):
best_protocol = StimProtocol(
stim_dur=1.8038, stim_min_isi=2.2538,
illumination_power_mw=1.7398,
n_pulses=5, pulse_width_frac=0.3415,
intensity_start=0.6379,
intensity_end=0.0192,
pre_stim_quiet_s=0.2729,
)

## Slide 12: Waveform Design
Goal was to maximize network recovery with some weighting for experiment duration. Other goals may have different shapes

## Slide 13: Key Parameters
Results are only as good as the calibration.
Literature or EM reconstruction for brain region
Paired patch-clamp recordings if available
Spontaneous activity recording
tau_ca_rise / tau_ca_decay | Indicator spec sheet or fit to step data
dF_F_max / noise_sigma | Peak dF/F from spec sheet; noise from dark frames
opsin_sensitivity_hz_per_mw | Patch-clamp power series.
conn_prob | Literature or EM reconstruction for brain region
w_excit_mean | Paired patch-clamp recordings if available
r_spont | Spontaneous activity recording
neuropil_r | Estimate from blank-shutter frames
N_cells, N_px_x/y | Acquisition system settings and ROI detection count

## Slide 14: Wrap Up
htb enables informed trades between protocol duration and anticipated experimental results

## Slide 15
htb — Connectivity Imaging Toolbox
Six capabilities in one framework:
Full biophysical simulation · Bayesian protocol search · Balanced E/I recovery
Cross-network robustness evaluation · PSP fitting · Drug screen simulation
For questions and collaboration